## Slide 1
Fotómetro
GEDA – Ing. Jacoby
Rev 1.0 - 2025

## Slide 2
Fotómetro
GEDA – Ing. Jacoby
Basado en el IC TSL2591

## Slide 3
Hardware Setup
GEDA – Ing. Jacoby
Micro USB
1- Wire the following circuit.
2- Flash tsl2591.ino on D1 mini.
Board: LOLIN(WEMOS)D1 R2 & mini
CPU :ESP8266

## Slide 4
Hardware Setup
GEDA – Ing. Jacoby
Fotómetro
USB
Fotómetro
Matlab genera 11 niveles de gris en la pantalla.
Por cada nivel generado el fotómetro envía la lectura a Matlab. Una vez almacenadas las 11 lecturas se calcula el valor de gamma.

## Slide 5
Tests
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab:
Measurement Loop
Generate 11 Gray Levels
USB Serie

## Slide 6
Montaje
GEDA – Ing. Jacoby
Fotómetro

## Slide 7
Tests: Samsung T24C550
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab
Results:

## Slide 8
Tests: Samsung T24C550
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab
Results:
Gamma Control | Measured Gamma
-3 | 1.6
0 | 1.8
+3 | 2.1

## Slide 9
Matlab Files
GEDA – Ing. Jacoby
Luxtest.m : Photometer Measurement Program
Luxmeter.m : Returns Light Luminosity in lux
Generarte_gray.m : Sets Gray level on screen.
Start
Last ?
Set Gray Level
Measure
(Luxmeter.m)
Next Gray Level
Adjust acquired data
Using
CFT (Curve fitting Tool)
and find out gamma
Plot Results,
Fitted Curve and Gamma
END
Luxtest.m

## Slide 10
Measurement setup and use
GEDA – Ing. Jacoby
1- Connect the photometer to USB to computer USB port
2- Find out the USB serial port on computer (COMxx)
3- Edit and modify serial port on luxmeter.m
ser = serial('COM1'); % Windows port style
ser = serial('/dev/ttyUSB0'); % Linux port style
4- Attach photometer as close a possible to monitor
5- Open matlab and run luxtest.m

## Slide 11
Measurement setup and use
GEDA – Ing. Jacoby
Notes: Each sample is taken every 2 seconds (defined on firmware)
Two samples are taken per gray level and averaged
(see Nmeas on luxtest.m)