## Slide 1
Fotómetro IoT
GEDA – Ing. Jacoby
Rev 2.0

## Slide 2
Fotómetro IoT
GEDA – Ing. Jacoby
Basado en el IC TSL2561

## Slide 3
Fotómetro Conectividad
GEDA – Ing. Jacoby
WIFI
Fotómetro
RS232
Cloud
IC2Cloud
Remote Access

## Slide 4
Fotómetro I/O
GEDA – Ing. Jacoby
Second TLS
OLED Display
Extension
5V – 1A
RS232 3.3V TTL
Reset
SCL
SDA
GND
3V3
ESP-07
5V
GND
5V
GND
TXD
RXD
N/C
GND Tip
(Baud Rate 115200)
Run[open]/Pgm[closed]
WiFi-Cloud
Enabled[open]/Disabled[closed]

## Slide 5
Photometer operating modes
GEDA – Ing. Jacoby
Cloud mode: when WIFI is available (yellow jumper open at power on)
Standalone mode: when WIFI is not available (yellow jumper closed at power on)
In both cases serial output is available . Output Rate: 1 sample every 2 seconds(1)
Cloud mode: Samples are sent to cloud and from cloud to phone apk (illuminance.apk)
WIFI parameters setup
Wireles router / AP / Hotspot Name : IOT_WIFI
Password: GEDA2016

## Slide 6
Tests
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab
Setup
Fotometer

## Slide 7
Tests
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab:
Measurement Loop
Generate 11 Gray Levels
USB Serie

## Slide 8
Tests: Samsung T24C550
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab
Results:

## Slide 9
Tests: Samsung T24C550
GEDA – Ing. Jacoby
Automated Gamma Measurement for LCD display using Matlab
Results:
Gamma Control | Measured Gamma
-3 | 1.6
0 | 1.8
+3 | 2.1

## Slide 10
Matlab Files
GEDA – Ing. Jacoby
Luxmeter.m : Returns Light Luminosity in lux
Luxtest.m : Photometer Measurement Program
Start
Last ?
Set Gray Level
Measure
(Luxmeter.m)
Next Gray Level
Adjust acquired data
Using
CFT (Curve fitting Tool)
and find out gamma
Plot Results,
Fitted Curve and Gamma
END

## Slide 11
Measurement setup and use
GEDA – Ing. Jacoby
1- Connect the photometer to USB to serial converter
2- Connect the photometer to power supply
3- Connect the USB serial converter cable to computer USB port
Find out the USB serial port on computer (COMxx)
5- Edit and modify serial port on luxmeter.m
ser = serial('COM1'); % Windows port style
ser = serial('/dev/ttyUSB0'); % Linux port style

## Slide 12
Measurement setup and use
GEDA – Ing. Jacoby
6- Attach photometer as close a possible to monitor
7- Open matlab and run luxtest.m
Notes: Each sample is taken every 2 seconds (defined on firmware)
Two samples are taken per gray level and averaged
(see Nmeas on luxtest.m)

## Slide 13
Schematic
GEDA – Ing. Jacoby

## Slide 14
APP: Illuminance.apk
GEDA – Ing. Jacoby
http://personal.ik.itba.edu.ar/~jacoby/ilum/